## Slide 1: Forward model summary
Updated 2023-05-22
Samuel Adams-Tew

## Slide 2: Goal
Create a useful forward model for MPME imaging
  Account for inhomogeneities and other variables that are typically not accounted for in modeling and inverse models for reconstruction
  Use forward model to move from parameter space to image space and use the image space values as loss for training the inverse model
  Potential to create simulated training data that may be useful in training neural networks to perform MR parameter mapping on real data?

## Slide 3: Bloch equation and variables
Solving Bloch equation with relaxation in the rotating frame.
is the magnetic moment in rotating frame
is the the gyromagnetic ratio of a species with arbitrary resonance frequency
is the external magnetic field in the rotating frame
and are the longitudinal and transverse relaxation times, respectively, at some point in space
is the equilibrium magnetization in the direction of the main magnetic field
In general, these variables may be functions of both position and time.
The current implementation allows for spatially varying , , and , and the external field may vary over space and time.

## Slide 4: Variables, continued
, where is the chemical shift between the species of interest and the on-resonance frequency. The standard equation for this shift is , and the shift of fat relative to water is
The external field is currently implemented with several components
  The main magnetic field with an additive component of spatial inhomogeneity, both solely along the z-axis
  Radiofrequency excitation as a separable function of the excitation envelope (on-resonance frequency demodulated) and a map of RF inhomogeneity. B1 has only x- and y-components
  Gradients vary linearly over space such that the strength of the field in the z-direction is a linear function of position

## Slide 5: B field, continued
The external field in the rotating frame is obtained by including a fictitious field that demodulates ”on-resonance” rotation where

## Slide 6: Simplification
Substitute , and simplify
This allows us to rewrite the Bloch equation in the rotating frame as where is an angular velocity vector for the axis and rate of precession of the magnetic moment.

## Slide 7: Two implementations
Euler method provides a first order approximation over a series of finite time steps, useful for comparison with toy examples but requires very small steps to sufficiently approximate rotational motion.
Symmetric operator splitting separates the rotation and relaxation effects, applying operators for the exact solution of the simpler problems of pure rotation and pure relaxation.

## Slide 8: Euler method
System of coupled equations
Solve with finite difference steps

## Slide 9: Euler method
% Compute angular velocity in rotating frame
omegaX = gamma*(1 + delta).*real(B1(iter)*B1map);
omegaY = gamma*(1 + delta).*imag(B1(iter)*B1map);
omegaZ = gamma*( delta*B0 + (1 + delta).*(B0map + B0drift(iter) + sum(grad(:, iter).*x)) );
% Compute cross product components (faster than using cross())
crossX = Mloop(2,1,:,:,:,:).*omegaZ - Mloop(3,1,:,:,:,:).*omegaY;
crossY = Mloop(3,1,:,:,:,:).*omegaX - Mloop(1,1,:,:,:,:).*omegaZ;
crossZ = Mloop(1,1,:,:,:,:).*omegaY - Mloop(2,1,:,:,:,:).*omegaX;
% Compute rate of change of in each component
dMxdt = crossX - Mloop(1,1,:,:,:,:)./T2(1,1,:,:,:,:);
dMydt = crossY - Mloop(2,1,:,:,:,:)./T2(1,1,:,:,:,:);
dMzdt = crossZ - (Mloop(3,1,:,:,:,:) - Meq)./T1(1,1,:,:,:,:);
% Update magnetization state
Mloop = [dMxdt; dMydt; dMzdt].*dt + Mloop;

## Slide 10: Symmetric operator splitting
Rotation matrix for a rotation about by
Axis angle rotation matrix
Relaxation (implemented as elementwise product of vectors)
Recovery

## Slide 11: Symmetric operator splitting
% Compute axis of rotation
axX = (1 + delta).*real(B1(iter)*B1map);
axY = (1 + delta).*imag(B1(iter)*B1map);
axZ = ( delta*B0 + (1 + delta).*(B0map + sum(grad(:, iter).*x)) );
% Compute half of rotation angle; note clockwise rotation
ang = -gamma*sqrt(axX.^2 + axY.^2 + axZ.^2) * dt/2;
% Compute rotation matrix
Rot = axis_angle_rotation_matrix([axX; axY; axZ], ang);
% Compute relaxation terms
[Rel, Rec] = relaxation(dt, T1, T2, Meq);
% Update magnetization state
Mloop = pagemtimes(Rot, Rel.*pagemtimes(Rot, Mloop) + Rec);

## Slide 12: Convergence testing
Apply a slice-selective 90° RF pulse with refocusing gradient and compare the magnetization state at the end of the simulation.

## Slide 13
Euler method
Symmetric operator splitting